## Slide 1: Treated Wood
Inorganic Arsenic Substance Information Sheet

## Slide 2: SUBSTANCE IDENTIFICATION
Inorganic Arsenic
Copper acetoarsenite, arsenic and all inorganic compounds containing arsenic except arsine, measured as arsenic (As)
Power Poles, Traffic Barriers, Rail Road Ties, Traffic Sign Posts
Landscaping,

## Slide 3: Permissible Exposure Limit.
0.01 milligrams per cubic meter of air (same as 10 micrograms per cubic meter of air) as determined as an average over an 8-hour period.
No employee may be exposed to any skin or eye contact with arsenic trichloride or to skin or eye contact likely to cause skin or eye irritation.

## Slide 4: Action Level
0.005 milligrams per cubic meter of air (same as 5 micrograms per cubic meter of air) determined as an average over an 8-hour period.

## Slide 5: Regulated Areas.
Only employees authorized by your employer should enter a regulated area.

## Slide 6: HEALTH HAZARD DATA
The health hazard of inorganic arsenic is high
Exposure to airborne inorganic arsenic may cause lung cancer, and it can be a skin irritant.
Inorganic arsenic may also affect your body if swallowed.
One compound in particular, arsenic trichloride, is especially dangerous because it is highly corrosive and it can be absorbed readily through the skin.
Because inorganic arsenic is a poison, you should wash your hands thoroughly prior to eating or smoking

## Slide 7: PROTECTIVE CLOTHING AND EQUIPMENT
Respirators.
Protective clothing. You must not eat, drink, smoke, chew gum or tobacco, or apply cosmetics in the regulated area, except that drinking water is permitted. If you work in a regulated area your employer is required to provide lunch rooms and other areas for these purposes.
If you work in a regulated area, your employer is required to provide showers, washing facilities, and change rooms. You must wash your face and hands before eating and must shower at the end of the work shift. Do not take used protective clothing out of change rooms without you employer's permission. Your employer is required to provide for laundering or cleaning of your protective clothing.

## Slide 8: SIGNS AND LABELS
When the PEL is exceeded, your employer is required to post warning signs and labels for your protection. Signs must be posted in regulated areas. The signs must warn that a cancer hazard is present, that only authorized employees may enter the area, and that no smoking or eating is allowed, and that respirators must be worn.

## Slide 9: MEDICAL EXAMINATIONS
If your exposure to arsenic is over the action level at least 30 days per year, or your have been exposed to arsenic for more than 10 years over the action level.
The physician must not tell your employer any conditions he or she detects unrelated to occupational exposure to arsenic but must tell you those conditions.

## Slide 10: OBSERVATION OF MONITORING
When Air Monitoring is conducted you have the right to know who and when the monitoring will happen. You or your representative may observe the monitoring. You will be advised of the air monitoring results.

## Slide 11: ACCESS TO RECORDS
You have the right to see the records for your physical exams and air monitoring results.

## Slide 12: TRAINING AND NOTIFICATION
Additional information on all of these items plus training as to hazards of exposure to inorganic arsenic and the engineering and work practice controls associated with your job will also be provided by your employer. If you are exposed over the permissible exposure limit, your employer must inform you of that fact and the actions he or she is taking to reduce your exposures